## Slide 1
Potential Environmental Drivers of Algal Blooms &
Utility of LANDSAT characterization of the James River
Dennie Truong, Colby College ‘24
Introduction
Discussion
Results & Models
Research Question
What environmental factors are driving algal bloom?
What is the efficacy of LANDSAT 8 data in characterizing blooms?
Background
Nutrient pollution (primarily from runoff and sewage effluent) often results in seasonal eutrophication, phytoplankton blooms and hypoxia in parts of the Chesapeake, especially during the summer months1,2.
Consequences of blooms includes3:
  Depletion of dissolved oxygen  fish kills
  Toxin release from HABs  results in wildlife mortality
     cause adverse health effects to local communities
  Clogging water treatment plants
Figure 1. Algal blooms in the James River near the Monitor Merrimac Bridge in August 2013. (Wolfgang Vogelbein/VIMS)
Figure 2. Extreme case of algal blooms leading to fish kills due to hypoxic conditions. (J.B. Forbes)
Methods
Study Site
A section of the James River at 5 stations from January 2013 to December 2022
About the Data
Monthly monitoring has occurred since the mid-1980s on water quality & phytoplankton
Collected by Maryland Department of Natural Resources, Morgan State University, Old Dominion & the Virginia Department of Environmental Quality (VDEQ)
Variable of Interest: Chl-a, Nutrients, Turbidity & Water Temperature
Launch on February 11, 2013 (still operational)
Bands of interest: Coastal aerosols, blue, green, red, near infrared
30-meter multispectral resolutions along a 185km swath
The blooms observed on the James may be driven by ammonium and phosphate availability, and water temperature.
On average, the head of the James experience higher volume of phytoplankton blooms than compared to the mouth of the river
It appears that algal bloom trends was not affected by the pandemic in 2020 (consistent with both GAM & CHL Models)
Figure 4. In situ Chl-a record as a function of time for the 5-sampling stations along the James River from January 2013 to December 2022.
Data Analysis: Conducted using
Generalized Additive Model (GAM)
NH4+ PO43
Chl-a
Turbidity
Water Temp.
Major factors that influence/drive the growth of phytoplankton are carbon, nitrogen, phosphorus and light4.
NITROGEN: Ammonium
Studies found that ammonium appears to be the primary inorganic nitrogen form that goes into synthetic reactions and is the most energetically favorable source of inorganic nitrogen because of its reduced state4.
PHOSPHORUS: Phosphate
Phytoplankton uses both phosphate and dissolved organic phosphorus, particularly at high substrate concentrations5.
TURBIDITY: May be a sign of greater sediments/detritus  Leading to enhance nutrients in the river for phytoplankton growth to an extent
WATER TEMPERATURE: Can affect the metabolism and hence the biological activity of organisms. Blooms around the Chesapeake Bay were found to be between 18.0-26.1 oC 6.
Marginal Mean Effects
Figure 5. GAM fitted line plotted over time from 2013 to 2022 across 5 stations. Confidence band signifies 95% with in-situ Chl-a measurements data plotted as points.
Chlorophyll Model
Using LANDSAT to characterize blooms
AUG 2022
JULY 2020
JULY 2019
A. PRE Pandemic
B. During Pandemic
C. POST Pandemic
(Developed by Isha Chinniah)
Variables excluded from analysis due to data availability:
Light & Carbon: Necessary for photosynthesis
Silica: Needed for growth of diatoms
Salinity: Determines whether freshwater or marine species of planktons are found along the James
Figure 7. Using chlorophyll model developed using principal component analysis by Isha (colleague), chl-a was derived using scores calculated based on LANDSAT bands (coastal, red, green, blue, near infrared). Map depicted shows model prediction spatially along the entire James River (A) on July 27, 2019, (B) on July 13, 2020, and (C) on August 4, 2022.
Acknowledgements
I would like to thank and recognize the following people for their contributions to my project! Also thank you to SARP East program for the opportunity, resource, and support throughout this summer!
Gina Ralph
(VIMS)
Susanne Craig
(NASA Goddard)
Ian Carroll
(NASA Goddard)
Bob Swap
(NASA Goddard)
Isha Chinniah
(SARP East Undergrad)
References
Figure 3. Image taken from Google Maps plotting the 5 stations along the James River.
Guildford and Hecky7: Suggested for lakes and oceans
N limitation occurred at TN/TP < 9
N and P co-limitation happens at TN/TP 9 to 22.
The James River is mostly a nitrogen limiting OR nitrogen and phosphorus co-limiting system
Figure 6. Marginal predictions for each of the environmental variables; shaded areas represent the 95% confidence intervals.
Proxy for: Phytoplankton
Algal bloom
CHL-a
CONCEPT MAP
Source: EnviroScience, Inc
By: Bill Curtsinger
Appears that increasing turbidity is associated with decrease in Chl-a
Speculation: Highly turbid environments limit space for phytoplankton growth
Phytoplankton driving turbidity  Shading light from more growth
Turbidity
Water Temperature
Appears that increasing water temperature is associated with increasing Chl-a
Speculation: Higher temperature  More sunlight  enhance photosynthesis reactions
The model explains 71.7% of the deviance. ( = 0.709, RMSE= 7.83, MAE = 5.43).
Increasing ammonium while holding phosphate constant:
At 0,25,50%: Shows phosphorus is limiting
At 75,100%: Shows nitrogen is limiting
NH4+, PO43 Interaction
Importance
Help identify algal blooms in other regions (using environmental drivers and spectral data)
Provide a stepping-stone for monitoring programs on HABS
LE5.1
RET5.2
TF5.5
TF5.5A
TF5.6